## Slide 1: Mini-Project 1
Gate-level netlist to def parser

## Slide 2: Inputs and Outputs
Inputs:
  Gate-level netlist in JSON format
  LEF file
  Standard Cell library (liberty file)
  Design options
Outputs:
  DEF file with the following sections
    Parsing rules
    Die area
    Rows
    Components
    PINS
    NETS
    Special NETS (VDD, GND)

## Slide 3: Die Area
DEF file specifies the lower left and upper right corner coordinates of the total die area.
Die area = Die width * Die height
Aspect ratio = Die Height/Die width
Die width = sqrt(Die area/Aspect ratio)
*Die width and height must be multiples of site width and height respectively

## Slide 4: Components
Each cell used in the GL-netlist is searched in the LEF and written in def file with the appropriate type.

## Slide 5: Rows
The die is divided into horizontal rows, were sites are placed beside each others.
Number of rows in calculated as follows:
  # rows = Die height/ Site height

## Slide 6: NETS
Internal and external connections
Search for nets in GL-Netlist JSON, check connected cells and list all nets, their connected cells/pins and the direction in which they are connected.
Example:
- a<1>
( AOI22X1_1 A )
( PIN a<1> )

## Slide 7: Power rings
Power Rings are, vdd and gnd, placed around the core area.
Metal spacings are extracted from the LEF file to separate gnd and vdd